## Slide 1
Classical Machine Learning Framework for Multi-Class sEMG Classification Using EMAHA-DB1
A classical ML-based system for 22-class ADL recognition using the EMAHA-DB1 sEMG dataset.
Koda Adam
S20230020312
Goluguri Nikhil Suri Reddy
S20230020302
Abraham Scariya
S20230020275
Kalla Sanjay Naidu
S20230020309
Indian Institute of Information Technology, Sri City

## Slide 2
Motivation & Problem Statement
Surface electromyography (sEMG) signal classification is a critical area in biomedical engineering, enabling intuitive human-machine interaction.
Real-World Impact
Enables advanced prosthetics, sophisticated rehabilitation tools, and responsive robotics, enhancing quality of life and functionality.
Complexity of ADL Recognition
Activities of Daily Living (ADL) classification presents significantly greater challenges compared to simple gesture recognition due to variability and contextual nuances.
Interpretability & Efficiency
There is a growing need for lightweight, interpretable classical machine learning models capable of handling this complexity efficiently.

## Slide 3
EMAHA-DB1 Dataset Overview
The EMAHA-DB1 dataset is a comprehensive resource for sEMG research, capturing a wide range of human activities.
Dataset Specifications
25 subjects participated in the data collection.
22 distinct Activities of Daily Living (ADL) were performed.
8-channel sEMG signals were recorded at a high sampling rate of 2000 Hz.
Activities are categorized by FAABOS (Feeding, Ambulation, Assessment, Body Positioning, Object Interaction, Self-Care).
Inherent Challenges
High Variability: Significant differences in sEMG signals across subjects and repetitions.
Class Overlap: Similar sEMG patterns for different ADL activities.
Imbalance: Uneven distribution of samples across different activity classes.
Noise: Presence of artifacts and electrical interference affecting signal quality.

## Slide 4
Preprocessing for Optimal Signal Quality
Robust preprocessing steps are essential to transform raw sEMG signals into a clean, standardized format suitable for feature extraction and classification.
01
DC Offset Removal
Eliminates constant bias from the sEMG signal, ensuring that signals are centered around zero and accurately reflect muscle activity.
02
Z-score Normalization
Standardizes signal amplitudes by subtracting the mean and dividing by the standard deviation, reducing inter-subject variability.
03
Windowing Technique
Applies a 250 ms window with a 50% overlap to segment the continuous sEMG data, creating discrete frames for analysis.
04
Output: Clean, Standardized Frames
The result is a set of clean and standardized EMG frames, perfectly prepared for the subsequent feature extraction stage.

## Slide 5
Comprehensive Feature Extraction (193 Features)
A rich set of 193 features was extracted to comprehensively describe the sEMG signals, capturing various aspects of muscle activity.
Time-Domain Features: Mean Absolute Value (MAV), Root Mean Square (RMS), Waveform Length (WL), Zero Crossings (ZC), Slope Sign Changes (SSC), Willison Amplitude (WAMP).
Frequency-Domain Features: Mean Frequency (MNF), Median Frequency (MDF), various band powers.
Statistical Features: Variance, Skewness, Kurtosis, Hjorth parameters (Activity, Mobility, Complexity).
Nonlinear Features: Entropy measures (e.g., Sample Entropy, Approximate Entropy), Fractal Dimension.
Autoregressive (AR) Coefficients: AR models of orders 1 through 10, capturing temporal dependencies.
Purpose: These features collectively capture amplitude, frequency content, signal complexity, and temporal patterns, crucial for discriminative classification.

## Slide 6
Strategic Feature Selection (Final 40 Features)
To optimize model performance, reduce overfitting, and improve computational efficiency, a multi-stage feature selection process was employed.
Correlation Filtering
Initial step to identify and remove highly correlated features, minimizing redundancy and multicollinearity.
Mutual Information Ranking
Features ranked based on their mutual information with the target variable, selecting the top 80 most informative features.
Random Forest Importance
Leveraged Random Forest to determine feature importance, leading to the selection of the final 40 most discriminative features.
Benefits: Reduced overfitting, faster training times, and enhanced model generalization capabilities.

## Slide 7
Machine Learning Models Employed
A suite of classical machine learning models was evaluated to determine the most effective approach for sEMG ADL classification.
XGBoost
Achieved the best performance with an accuracy of 73%, demonstrating its robustness for complex, high-dimensional data.
Fine + Ensemble KNN
Performed commendably with 70% accuracy, benefiting from the reduced feature set and ensemble methodology.
Random Forest
Showcased solid performance at 67%, providing a good balance between accuracy and interpretability.
SVM Cubic
Exhibited the weakest performance at 57%, indicating limitations in handling the inherent heterogeneity of sEMG data.
All models were trained using the same optimized 40-feature vector to ensure a fair and consistent comparative analysis.

## Slide 8
Results & Key Findings
The comparative analysis of various classical machine learning models revealed distinct performance characteristics for sEMG ADL classification.
XGBoost Dominance
Demonstrated the strongest class separation and highest accuracy, attributing its success to efficient handling of non-linear relationships.
KNN's Efficacy
Performed well, likely due to the reduced dimensionality and improved feature space after selection, enhancing nearest neighbor identification.
Random Forest's Role
Achieved moderately effective results, highlighting its ability to manage complex data while mitigating overfitting.
SVM Challenges
Struggled with the heterogeneity and potentially non-separable nature of the sEMG data, leading to lower performance.
At the FAABOS category level, Ambulation activities were the easiest to classify, while Object Interaction posed the greatest challenge.

## Slide 9
Limitations & Future Improvements
While promising results were achieved, several areas for improvement and further research have been identified.
Evaluation Split Strategy
The current evaluation used a subject-dependent split; a more rigorous Leave-One-Subject-Out (LOSO) cross-validation is needed to assess generalizability.
Dataset Expansion
Increasing the number of subjects in the EMAHA-DB1 dataset will significantly enhance the robustness and reliability of the models.
Advanced Feature Exploration
Investigating wavelet-based features (e.g., DWT, CWT) could capture transient sEMG characteristics more effectively.
Hybrid & Stacked Models
Exploring hybrid or stacked model architectures may leverage the strengths of multiple classifiers for improved accuracy.
Deep Learning Baselines
Benchmarking against deep learning models (CNN, LSTM, Transformers) would provide valuable insights into comparative performance.
Real-time Deployment
Future work should include testing the system's performance and feasibility in real-time deployment scenarios.

## Slide 10
Team Contributions
This project was a collaborative effort, with each team member bringing specialized expertise to contribute to its success.
Koda Adam
Responsible for feature extraction methodologies and XGBoost training.
Goluguri Nikhil Suri Reddy
Developed and optimized the Fine + Ensemble KNN model.
Abraham Scariya
Implemented the Random Forest model and conducted comprehensive confusion matrix analysis.
Kalla Sanjay Naidu
Developed the SVM (Cubic) model and optimized it.
Joint Work: Dataset handling, extensive literature review, final report compilation, and presentation development were collaborative efforts across the entire team.